## Slide 1: AI Face Algorithm Evaluation Method Design
Wang Tianyue | 2022/06/20
AI & PCIE Validation Team

## Slide 2
Variable | Matrices | Description | Data rate
Pitch | Up | α move between 0 to -15 | 50%
 | Forward | Do not move | 0%
 | Down | α move between 0 to 15 | 50%
Yaw | Left | β move between 0 to -15 | 50%
 | Forward | Do not move | 0%
 | Right | β move between 0 to 15 | 50%
Roll | Clockwise | γ move between 0 to -15 | 50%
 | Steady | Do not move | 0%
 | Counterclockwise | γ move between 0 to 15 | 50%
Mouth | Close & Open | Just speak or open one’s mouth | 100%
Eye | Eyebrow | Just move | 50%
 | Eyelid | Just move (close or open one's eye) | 50%
Light | Weak | 30<lux<75 | 20%
 | Medium | 75<lux<200 | 40%
 | Strong | 200<lux<500 | 20%
 | Uneven | ¦lux(left) – lux(right)¦>150 | 20%
AI Face Algorithm Evaluation Method Design -Test set collection
Explanation: Variable pitch, yaw, row means to evaluate the movements of head, while variable mouth, eye focus on the facial movements. The optical flow is easily affected by light condition, so different light environments are defined. Meanwhile, we measure the horizontal movement of head.
The collection only use laptop camera. Use the collection tool provided by Ruifeng for saving input and output videos. Use the input video as the driving video and ground truth, several selected images can be used as source image. The evaluation will happen between the driving video and output video.
Prepare to take 70 videos which each of them last for at least 5 seconds. Take 10 videos for one variable. Data rate 10% represents one video. It'll be better to have multiple participants for one variable. Prepare to cover at least 7 participants.
Dimension
Motion transfer: angle
Expression transfer
Optical flow
Motion transfer: horizontal | Horizontal move | Left | Head moves left horizontally | 50%
 |  | Right | Head moves right horizontally | 50%